ＰＣＢProcessing technology requirements specification

1.Basic process information
Layers	8	Plate type	FR4
Finished plate thickness	1MM	Finished sheet thickness tolerance	＋／－１０％
ＰＣＢAcceptance Criteria	National Military Standard	Finished Dimensional Tolerance	＋／－０．１５ｍｍ
Surface treatment	BGA adopts OSP process	Warpage	0.75%
Solder mask color	blue	Via Process	plug hole
Character color	white	Craft side

Stackup Information
Finished Thickness(mm):1.0±0.1
AccountThickness(mm):0.97
LAYER STACKING

TOP			0.5oz +Plating
	PP(3313)	3.91
GND02			0.5oz
	Core	5.12
ART03			0.5oz
	PP(1080*2)	5.47
GND04			0.5oz
	Core	3.94
ART05			0.5oz
	PP(1080*2)	5.47
ART06			0.5oz
	Core	5.12
GND07			0.5oz
	PP(3313)	3.91
BOTTOM			0.5oz +Plating

SINGLE IMPEDANCE：
	layer	width(mil)	impedance(ohm)	ref layer
	L1/L8	6	50	L2/7
	L3/L6	4.8	50	L2/4;L5/7

DIFFERENTIAL IMPEDANCE:
	layer	width/space(mil)	impedance(ohm)	ref layer
	L1/L8	4.5/9	100	L2/7
	L3/L6	4.5/9	100	L2/4;L5/7
	L1/L8	5\9	90	L2/7
	L3/L6	5\9	90	L2/4;L5/7

The board factory can adjust the line width according to the actual stack to achieve the purpose of controlling the impedance
3. Screenshot of Impedance Control

Yellow wire control 100ohm (L3)
Red line width control 90ohm (L3)

Yellow line width control 100ohm, (L6)

Red line width controlled 90ohm impedance (L6)